## Slide 1: H2-Transportoptionen
15.12.23 | Markus Albuscheit | Strommarkttreffen
CONFIDENTIAL AND PROPRIETARY
Any use of this material without specific permission of HYDROGENIOUS LOHC TECHNOLOGIES is strictly prohibited
Verschiedene Perspektiven im Blick

## Slide 2
Hydrogen Economy: Chicken-Egg-Problem
Question: Which basket to transport eggs from/to the chicken?
Problem definition

## Slide 3: What I am not focusing on
Scope of Presentation
Import vs. Export of Hydrogen  Market prices and availability are determining
Electricity vs. Hydrogen  End use and costs are the key criteria
What I am focusing on
 Possible hydrogen transport options and key decision criteria
What is the optimal basket for my egg?
Technologies: Ammonia (NH3), Liquid Hydrogen (LH2), Liquid Organic Hydrogen Carriers (LOHC), Pipelines to a certain extent

## Slide 4: There are three relevant criteria for evaluating hydrogen transport options
Carrier Density
H2-Purity
Use of existing infrastructure
Demand and supply of hydrogen or hydrogen derivative
GHG-Emissions
Cost Efficiency
Use of existing infrastructure, i.e., port terminals, storage, ships & pipelines
Technology readiness level (TRL)
Availability
Regulatory Framework
Public Acceptance
Safety
Main topics

## Slide 5: 1. Cost Efficiency

## Slide 6: The cost efficiency is heavily depending on the assumptions of the model
Cost Efficiency
Source: Hampp et al. (2023); https://doi.org/10.1371/journal.pone.0281380
Authors conclusion: “no single exporter or Energy Supply Chain shows a unique techno-economic advantage over the others”
Levelised Cost of Hydrogen (LCoH) for Energy Supply Chains to Germany
Important cost-drivers:
H2-Purity (98 vs. 99.5 %)
Existing infrastructure
Hydrogen or hydrogen derivative
Energy cost for (Re-) Conversions
Utilization of Pipeline/Infrastructure
Safety & regulatory measures

## Slide 7
Best practice:
Meta-Analysis with several studies and assumptions
Worthy of discussion:
Modeling based on few sources and unrealistic assumptions
Cost Efficiency
Hydrogenious TCO Comparison (2023)
Supply costs of green chemical energy carriers at the European border: A meta-analysis,
Genge et. al. (2023)
Optionen für den Import grünen Wasserstoffs nach Deutschland bis zum Jahr 2030, ESYS
Staiß, F. et al. (2022)
NH3-Cracker CAPEX based on deuterium cracker
Large differences in H2-throughput between options
Technology Review of H2 Carriers; IRENA (2022)
Assumptions for carriers vary heavily
Cost parity of the main hydrogen carriers throughout the study landscape.
 It really comes down to qualitative factors, which are usually not included in many analysis!

## Slide 8: 2. Availability

## Slide 9: The availability of the transport option can be a huge bottleneck
Availability
Storage density
54 kgH2/m3LOHC-BT
62 kgH2/tLOHC-BT
Storage at ambient conditions
LOHC-BT
115 kgH2/m3NH3
170 kgH2/tNH3
Storage at -33 °C at cryogenic conditions
71 kgH2/m3NH3
Storage at -253 °C at cryogenic conditions
Existing global fleet
Ammonia (incl. Cracking)
Liquified H2
Potential vessel transport & hydrogen transport volumes
  Potential transport in Very Large Crude Carriers
    VLCC (280,000 DWT) can carry 17,000 tonnes of hydrogen
    Upgrade to 450,000 DWT* possible
  Transport in LPG vessels
    80k m3 LPG vessel can carry 9,800 tonnes of hydrogen
    If LNG-ships can be repurposed +200
  Transport in LH2 vessels
    The only existing LH2 vessel ‘Suiso Frontier’ from Kawasaki can potentially carry 9,000 tonnes of hydrogen
    But currently carries only 75 tons
  ~ 800 vessels
  ~ 50 vessels
  1 vessel
  *DWT = Deadweight tonnage
= 100 vessels
      IEA: Meeting the potential tripling of NH3 trade, building enough NH3 tankers could create bottlenecks in the short term.
Source: IEA, Global Hydrogen Review 2023, Page 123

## Slide 10: TRL - all technologies still have to mature and be scaled up to ensure availability
Availability
Basically, all large-scale projects that are considered and calculated already, are not feasible yet!
Source: IEA, Global Hydrogen Review 2023, Page 123

## Slide 11: 3. Safety

## Slide 12: How can we enable a safe hydrogen supply chain?
Or: How to keep the egg from breaking?
Safety
Hazard & toxicity profile
LOHC-BT
= Physical hazard
= Acute toxicity
= Envr. toxicity
= Low hazard/toxicity lvl.
= Medium hazard/toxicity lvl.
= High hazard/toxicity lvl.
Ammonia (incl. Cracking)
Liquified H2

## Slide 13: Always look at all these criteria to evaluate H2 transport options
Carrier Density
H2-Purity (98 va. 99.5 vs. 99.9997 %)
Use of existing infrastructure
Demand and supply of hydrogen or hydrogen derivative
GHG-Emissions (H2 leakage, N2O, CO2, …)
Cost Efficiency
Use of existing infrastructure, i.e., port terminals, storage, ships & pipelines
Technology readiness level (TRL)
Availability
Regulatory Framework
Public Acceptance
Safety
Summary

## Slide 14: Let’s carry the new energy world together.
HYDROGENIOUS LOHC TECHNOLOGIES GmbH Weidenweg 13 91058 Erlangen/Germany www.hydrogenious.net info@hydrogenious.net
Markus Albuscheit Strategic Analytics and Modeling

## Slide 15: How to locally store the transported hydrogen? Especially, if natural gas storage not sufficient/not usable for hydrogen
Or: How to store the eggs?
Availlability
Storage
LOHC-BT
Ammonia (incl. Cracking)
Liquified H2
Use of widely existing infrastructure for
liquid oil infrastructure
NH3 infrastructure available in selected ports & areas
New infrastructure to be build up from scratch
 „Rocket Science“

## Slide 16: Qualitative Comparison of Hydrogen Transport Options
 | Ammonia incl. H2-Release/Cracking (NH3) | Liquid Hydrogen (LH2) | Liquid Organic Hydrogen Carriers (LOHC) | Pipeline Transport
Technological Readiness | ̶ | o | ̶ | o
Flexibility | o | + | o | ̶
Safety | o | o | ++ | ++
Scalibility | + | ̶ | + | +
Implementability | + | o | + | +